# Text boxes

2

3

1

NEW

OLD

Modifications:

- The plastic floor flange changed into press-brass flange, cartridge will be 5 mm longer.

- Sealing outwards through 2 o-ring gaskets (flange and device). Refill will be replaced though a complete device.

- The change of the device will be carried out on the lower surface (brass-flange). The whole cartridge don´t have be changed (see enclosure: change the device)

OLD

NEW

NEW

OLD

Difference between

AQA-total cartridge old / new

(since cartridge Nr. 236000)

6

5

4

3

2

1

OPEN

A.  Dismounting of used devices

- Remove and deplete the cartridge from AQA-total.

- Demount the cup nut of the brass-flange with the key which will be delivered with the device.

- Move the key clockwise.

- By dismantling of the cup nut the device will be removed too.

- Loose the cup nut from the brass-flange.

- Remove the device from the cartridge.

Change the device by

AQA-total cartridge new

(since cartridge Nr. 236000)

2a

2b

3

1

B. Installation

(mounting of the new device)

- To unpack the new device.

- Watch the mounting direction (devices can be mounted just in one direction):

2 a. At the flange there are 2 cuts

(recesses) with different

broadness,  180° displaced

2 b.  The broadness of the cut have

to comply with the mounting

link.

- Install device into the cartridge.

Change the device by

AQA-total cartridge new

(since cartridge Nr. 236000)

9

6

4

CLOSE

5

8

7

B. Installation

(mounting of the new device):

- Abandon the device from the flage.

- Put in the cup nut into the mounting link.

- Turn back the cup nut at the brass-flange with delivered 8-kant key.

- Turn the key clockwise.

- Tigthen up the cupnut til – the limit Stop of the flange.

- Jf is completed, please mount the cartrudge to the AQA-total.

Change the device by

AQA-total cartridge new

(since cartridge Nr. 236000)